## Slide 1: A Proposed Framework for Detecting and Replaying Problematic Modbus TCP Traffic on a Physical or Simulated ICS Testbed
William Johnson
Shiva Jyothi Angala
Pavan Madduri

## Slide 2: AIM
Develop a framework that will allow for the detection of potentially malicious traffic in a Modbus TCP-based industrial control system network as well as the replay of that potentially malicious traffic from traffic capture files.
This project is primarily a network forensics project.

## Slide 3: INTRODUCTION
The framework is intended to allow for replay of malicious traffic on a simulated (and possibly physical) industrial control system testbed using Modbus TCP traffic.
ICS testbed is used as honeypot, which can replay the detected attacks on the system.
The completed system consist of components:
  Network Security Monitoring
  Traffic replay engine

## Slide 4: Network Security Monitoring
Possible to monitor the state of a system at the application level, as well as modifying it as Modbus traffic is detected.
Bro provides a rich scripting language facilitates event handling (such as upon a read or write of a Modbus coil), data structures that can be maintained globally or locally, and functions to provide for easy modularization of behavior.

## Slide 5: Why Bro?
Network analysis framework that is much different from typical IDS
  Adaptable
  Efficient
  Flexible
  Open Source
  and yes Commercially Supported

## Slide 6: Continued..
Bro monitors traffic from live or captured sources.
Initially we go with packet captures, as the project progresses, once the system is joined, it will work with live traffic, creating packet capture files of indeterminate length as certain events are detected by Bro.

## Slide 7: Bro System State Model
In order to test Bro’s functionality in this regard, we built an example system.
Software simulated Water tank with three components that are attached to the PLC are:
  The water level in the tank
  A pumping system and
  A drainage valve
  When pump is ON/OFF – Blue light is illuminated respectively
  The state of the drainage valve is represented by the green and red lights:
  when the valve is closed - the red light is illuminated, and when it is open,
  the green light is illuminated.
  the yellow light is illuminated if the tank is full (the water level is 100 units)

## Slide 8: Continued..
The water limit level is 100, and assume that the tank is an open tank, so if the pump is activated at that limit, the tank simply overflows.
If the pump is on and the drain valve is closed, the water level is incremented by 1 unit per second.
If the pump is off and the drain valve is open, the water level is decremented by 1 unit per second, until the water level is 0. The water flow logic is implemented simply by timers.
Provides access to Modbus.
The valve and pump conditions are stored as coils.

## Slide 9: Bro Water Tank State Model
type Model: record {
water_level: count;
valve_closed: bool;
pump_on: bool;
};

## Slide 10: Water Tank Event Handler
event modbus_write_single_coil_response(c: connection, headers: ModbusHeaders, address: count, value: bool) {
if (address == 0) {
model$pump_on = value;
}
if (address == 1) {
model$valve_closed = value;
}
check_sanity();
}

## Slide 11: Critical State Check
function check_sanity() {
if (model$valve_closed == F && model$pump_on == T) {
print “ALERT: Pump enabled with unsealed drainage valve”;
}
if (model$pump_on == T && model$water_level >= 100) {
print “ALERT: Pump enabled with full container”;
}
}

## Slide 12: Forensic Traffic Interception and Replay
Modbus traffic captures can be replayed
Visual attack replay on physical or simulated testbed
For each Modbus packet:
  Establish connection with destination slave device on network if not existing
  Pause for traffic timing
  Send the Modbus request to the device
Tested on network with one and two PLCs—replay to multiple slave devices does work

## Slide 13: Challenges
Automatic slicing of packet capture file by Bro upon first malicious write—may require hacking on Bro source
Automatic recreation of system state before malicious traffic replay—especially on physical testbeds

## Slide 14: FUTURE WORK
First and foremost, if the Bro system is modified in order to automatically begin packet capture at the onset of a significant event, this would reduce the manual work required to prepare packet captures for system replay.
The system could be modified in order for Bro to function on live traffic, creating packet capture files as needed rather than running on existing packet captures that must be modified to isolate the beginning of malicious or otherwise suspect network communications.
Need functionality to bring testbed to its equivalent state during the initial attack before replay
  Manageable on simulated testbed; slightly more difficult on physical testbed
More than just Modbus!
  However, other protocols may require deep packet inspection to modify sequence numbers, etc.

## Slide 15: CONCLUSION
Implemented portions of a framework that provides for critical state monitoring using Bro network security monitoring as well as replay of suspect traffic over a Modbus TCP ICS network.
Application-level state modeling is used to identify the malicious traffic through packet capture.
Replay application allows a forensic analyst to replay packet captures to review the behavior of the system.
Functionality that should be in the future, automated through communication of the system with the testbed.

## Slide 16: REFERENCES
The Bro Project. 2014. The Bro Network Security Monitor [Online]. Available: https://www.bro.org
A. Carcano, A. Coletta, M. Guglielmi, M. Masera, I. Nai Fovino, and A. Trombetta. “A Multidimensional Critical State Analysis for Detecting Intrusions in SCADA Systems” in IEEE Transactions on Industrial Informatics, vol. 7, no. 2, May 2011.
I. Nai Fovino, A. Coletta, A. Carcano, and M. Masera. “Critical State-Based Filtering System for Securing SCADA Network Protocols” in IEEE Transactions on Industrial Electronics, vol. 59, no. 10, October 2012.
Scapy [Online]. Available: https://www.secdev.org/projects/scapy
G. Collins. Pymodbus [Online]. Available: https://github.com/bashwork/pymodbus